Example 2.1 Pad foundation with vertical central load on dense sand

Note: this is a persistent design situation; for simplicity, accidental design situations do NOT need to be checked.

| Question | Instruction | Answer |
| --- | --- | --- |
| GENERAL |
| 1 | Please provide your contact details in case we need to clarify your submission* | *Will be kept strictly confidential | Name Affiliation Email address |
| 2 | How many structures of this kind have you previously designed? | Tick one | ( None ( 1-2 ( 3-6 ( More than 6 |
| 3 | Having completed your design to Eurocode 7, how confident are you that the design is sound? | Tick one | ( Very unsure ( Unsure ( Confident ( Very confident |
| 4 | How did you account for the location of cone tests relative to the foundation? | Tick one | ( Did not consider test location ( Considered nearest test only ( Considered ‘average’ of all tests ( Considered trend of all tests, biased towards nearest ( Other (specify) … |
| 5 | Please explain the reasons for your answer to Q4 | Free text |  |
| SERVICEABILITY LIMIT STATE |
| 6 | Which parameters did you use for the SLS design of the spread foundation? | Tick all that apply | ( Cone resistance qc ( Cone sleeve friction fs ( Young’s modulus of elasticity E´ ( Poisson’s ratio ( ( Shear modulus of elasticity G ( Other (specify) … |
| 7 | What correlations did you use to derive soil parameter values (if used) for the SLS verification? If more than one, please list others below | Free text | Description: Author: Title: Pages: |
| 7a | Any other correlations? (please give same info as above) | Free text |  |
| 8 | What assumptions did you make in choosing these correlations? | Free text |  |
| 9 | How did you account for any variation in parameters with depth? | Tick one | ( Ignored variation with depth ( Assumed linear variation ( Assumed bi-linear variation ( Assumed stepped variation ( Other (specify) … |
| 10 | Please explain the reasons for your answer to Q9 | Free text |  |
| 11 | What is the characteristic value of qc at these depths? | Provide values in units of MPa | At 1 m, qc = | At 2 m, qc = | At 4 m, qc = |
| 12 | What is the characteristic value of E´ for a linear elastic calculation at these depths? | Provide values in units of MPa | At 1 m, E´ = | At 2 m, E´ = | At 4 m, E´ = |
| 13 | How did you assess these values? | Tick all that apply | ( By eye ( By linear regression ( By statistical analysis ( From an existing standard (specify) … ( From a published correlation (specify) … ( Comparison with a previous design ( From the soil description, not using the data ( Other (specify) … |
| 14 | Which calculation model did you use to determine settlement? | Tick one | ( Annex F.1 from EN 1997-1 ( Annex F.2 from EN 1997-1 ( Annex D.3 from EN 1997-2 ( Annex D.4 from EN 1997-2 ( Annex D.5 from EN 1997-2 ( Alternative from national annex (specify) … ( Alternative from national standard (specify) … ( Finite element analysis ( Finite difference analysis ( Other (specify) … |
| 15 | What width does the foundation need to avoid a serviceability limit state? | Provide value in m | BSLS = |
| ULTIMATE LIMIT STATE |
| 16 | Which parameters did you use for the ULS design of the spread foundation? | Tick all that apply | ( Cone resistance qc ( Cone sleeve friction fs ( Angle of shearing resistance (´ ( Effective cohesion c´ ( Angle of interface friction ( ( Other (specify) … |
| 17 | What correlations did you use to derive soil parameter values (if used) for the ULS verification? If more than one, please list others below | Free text | Description: Author: Title: Pages: |
| 17a | Any other correlations? (please give same info as above) | Free text |  |
| 18 | What assumptions did you make in choosing these correlations? | Free text |  |
| 19 | What is the characteristic value of (´ at these depths? | Provide values in degrees | At 1 m, (´ = | At 2 m, (´ = | At 4 m, (´ = |
| 20 | Which calculation model did you use to determine bearing resistance? | Tick one | ( Annex D from EN 1997-1 ( Alternative given in a national annex (specify) … ( Alternative given in a national standard (specify) … ( Terzaghi ( Meyerhof ( Brinch-Hansen ( Finite element analysis ( Finite difference analysis ( Other (specify) … |
| 21 | Which country’s National Annex did you use to interpret EN 1997-1? | Free text |  |
| 22 | Which Design Approach did you use for verification of the Ultimate Limit State (ULS)? | Tick one | ( Design Approach 1 Combinations 1 and 2 ( Design Approach 1 Combination 1 only ( Design Approach 1 Combination 2 only ( Design Approach 2 ( Design Approach 2* ( Design Approach 3 ( Other (specify) … |
| 23 23a | What values of partial factors did you use for this ULS verification? | Provide values | 1st combination | 2nd combination (if used) |
|  |  |  | (G | (Q | (G | (Q |
|  |  |  | (( | (c | (( | (c |
|  |  |  | (Rv | (Rd | (Rv | (Rd |
| 24 | What width does the foundation need to avoid an ultimate limit state? | Provide value in m | BULS = |
| 25 | What are the structural forces (at its centre-line) that the foundation must be designed for according to Eurocode 2? | Provide values in kNm and kN | Design bending moment MEd = | Design shear force VEd = |
| CONCLUDING QUESTIONS |
| 26 | What other assumptions did you need to make to complete your design? | Free text |  |
| 27 | Please specify any other data that you would have liked to have had to design this type of foundation | Free text |  |
| 28 | How conservative do you consider your previous national practice to be for this design example? | Tick one | ( Very conservative ( Conservative ( About right ( Unconservative ( Very unconservative |
| 29 | How conservative do you consider Eurocode 7 (with your National Annex) to be for this example? | Tick one | ( Very conservative ( Conservative ( About right ( Unconservative ( Very unconservative |
| 30 | How does your Eurocode 7 design compare with your previous national practice? | Tick one | ( Much more conservative ( More conservative ( About the same ( Less conservative ( Much less conservative |
| 31 | Please provide any other relevant information needed to understand your solution to this design exercise | Free text |  |
| PLEASE SUBMIT YOUR ANSWERS AT www.eurocode7.com/etc10/Example 2.1 THANK YOU FOR YOUR CONTRIBUTION! |